## Slide 1: EDES 301 Project Proposal Remote Controlled, Music Streaming, Self-Balancing Robot
October 5th, 2025
Joshua Aviles

## Slide 2: Background Information
Project Proposal
A two wheeled robot that uses two Nema 17 stepper motors and a PID algorithm to self-balance and move around
Wireless controller uses ESP32 and joystick modules to send out commands to robot’s motors and LED display
PocketBeagle uses a USB Bluetooth module in order to wirelessly communicate with controllers ESP32 (PocketBeagle is used instead of another ESP32, like in other projects)
A 16x32 RGB LED display allows for facial expressions and displays songs played on speaker (addition to previous projects)
Robots USB speaker connects to IOS system in order to stream music from an app (addition to previous projects)

## Slide 3: System Block Diagram
14.8V LiPo Battery
A4988 Motor Drivers
A4988 Motor Drivers
HiLetgo 12V to 5V Converter
USB Speaker
16x32 LED Display
PocketBeagle
IMU
NEMA 17 Stepper Motor
NEMA 17 Stepper Motor
Vmot
GPIO
Step
Dir
En
Sleep
1A
1B
2A
2B
1A
1B
2A
2B
Powered USB Hub
P2_9 to SCL
P2_11 to SDL
Bluetooth USB Adapter
Powered USB Hub
CLK
LA
OE
13 GPIO Pins
ESP32 WROOM 32
Joystick Module
Joystick Module
Bluetooth Serial (SPP)
VRx
Vry
SW
VRx
Vry
SW
5V LiPo Battery
Voltage
Divider

## Slide 4: Power Block Diagram – Robot Components
OVONIC LiPo Battery
14.8V
1300mAh
A4988 Motor Driver
Motor
Input: 22.2W = (14.8V)(1.5A)
Output: 5.175W = (3.45V)(1.5A)
Logic(From PocketBeagle)
Input: 33mW = (3.3V)(10mA)
HiLetgo 12V to 5V Converter
Input: 14.8V
Output: 5V
NEMA 17 Stepper Motor
Input:
5.175W = (3.45V)(1.5A)
USB Speaker
Input: 3W = (5V)(600mA)
A4988 Motor Driver
Motor
Input: 22.2W = (14.8V)(1.5A)
Output: 5.175W = (3.45V)(1.5A)
Logic(From PocketBeagle)
Input: 33mW = (3.3V)(10mA)
NEMA 17 Stepper Motor
Input:
5.175W = (3.45V)(1.5A)
IMU Sensor
Input: 33mW = (3.3V)(10mA)
PocketBeagle
Input: 2.5W = (5V)(500mA)
Output: 33mW = (3.3V)(10mA)
16x32 LED Display
Input(max):
12.5W = (5V)(2.5A)

## Slide 5: Power Block Diagram – Controllers Components
Joystick Module
Input: 25mW = (5V)(5mA)
Joystick Module
Input: 25mW = (5V)(5mA)
5V LiPo Battery
Output:
858mW = (5V)(260mA)
ESP32 WROOM 32
Input:
825mW = (3.3V)(250mA)
Voltage Divider

## Slide 6: Components / Budget
Component | EDES301 to Buy? | Cost
NEMA 17 Stepper Motors (2) – Amazon Link | Yes | $19.98
A4988 Motor Drivers (5) – Amazon Link | Yes | $10.19
Joystick Modules (2) – Amazon Link | Yes | $2.66
USB Speaker (1) – Amazon Link | No | $16.98
USB Bluetooth (1) – Amazon Link | No | $9.99
IMU (1) – Amazon Link | Yes | $2.10
OVONIC 4S 14.8V 1300mAh LiPo Battery (1) – Amazon Link | No | $18.99
12V to 5V Converter (1) – Amazon Link | No | $8.89
ESP32 WROOM 32 (1) – Amazon Link | No | $8.99
5V LiPo Battery (1) – Amazon Link | No | $20.99